## Slide 1
A FIELD GUIDE
5G Core Lab-in-a-Box
A complete 5G network in software — the big picture, the architecture, and the security loop, all in plain language.
Part 1 Big picture
Part 2 Architecture
Part 3 Security loop

## Slide 2
WHAT'S INSIDE
Three parts, one story
1
The big picture
What a 5G network is, what we installed, and how a phone gets online — with the club-staff analogy.
2
Reading the architecture
A guided tour of the components diagram: the colors, the RAN, the core's brains, the data gateway, and the two end-to-end journeys.
3
Reading the security loop
A guided tour of the attack-flow diagram: inject → tap → parse → score, and the five attacks with their tells.
5G Core Lab-in-a-Box · Field Guide
2

## Slide 3
PART 1
The Big Picture
What it is, what's installed, and how it works.

## Slide 4
THE BIG PICTURE
What is this, really?
A real 5G network is three things: a phone with a SIM, a cell tower, and a “core” in a data center that decides who gets on and routes their data. Normally that's rooms of expensive hardware spread across a city.
Here, every piece is software — all on one computer, talking to each other exactly the way the real hardware would.
Phone
Tower
Core
5G Core Lab-in-a-Box · Field Guide
4

## Slide 5
WHAT'S INSTALLED
The four building blocks
UERANSIM the phone & the tower
One program that simulates both a handset and a 5G radio. No SIM cards, no hardware — it exchanges the same messages a real phone and tower would.
Open5GS the core “brains” — about a dozen containers
Like the staff of a members' club: one checks your SIM, one registers you, one opens your session, one enforces the rules, a directory lets them find each other.
UPF the data gateway — runs on the host
The doorway your actual traffic flows through on its way out. Runs directly on the machine (our workaround for a kernel quirk).
Security tooling attack & capture — the whole point
Generate malformed or flood traffic on the core's internal pipes, record it, and train a model to tell normal from malicious.
5G Core Lab-in-a-Box · Field Guide
5

## Slide 6
HOW IT WORKS
Getting a phone onto the network
1
Find the tower
2
Prove the SIM
3
Register
4
Open a session
5
Get an IP
✓
In our lab this fully works. The simulated phone registered, authenticated, opened a session, and was assigned the address 10.45.0.2 — a working connection through the core.
5G Core Lab-in-a-Box · Field Guide
6

## Slide 7
THE PLUMBING
The pipes that matter
N2
The conversation
Signaling between the tower and the core — “let this phone on.”
NGAP
N3
The data tunnel
Your actual traffic, wrapped up and carried between tower and gateway.
GTP-U
N4
The control link
The core telling the data gateway how to handle each session.
PFCP
These three pipes — especially N3 and N4 — are exactly what the security tooling targets.
5G Core Lab-in-a-Box · Field Guide
7

## Slide 8
STATUS
Where it stands today
Working
5G core
Registration, auth, PDU session, N4 & N3 all verified end-to-end.
10.45.0.2
UE connected
A simulated phone attached and got a working data session.
N3 + N4
Traffic flowing
User-plane and control-plane pipes carry live traffic to capture.
Optional
Internet egress
One host-networking quirk on a non-standard kernel; not needed for the lab work.
5G Core Lab-in-a-Box · Field Guide
8

## Slide 9
PART 2
Reading the Architecture
A guided tour of the components diagram.

## Slide 10
FIRST, THE COLORS
How to read the diagram
Every line is colored by what it carries. Learn these four and the whole picture reads itself.
User-plane data Your actual traffic — web, video, everything you send and receive. (N3, N6)
Control / signaling The network talking to itself to set things up — no user data. (N2, SBI)
N4 · PFCP One specific control link: the core telling the data gateway how to run a session.
Lab tooling The security add-ons — generating attacks and recording traffic.
5G Core Lab-in-a-Box · Field Guide
10

## Slide 11
ORIENTATION
The whole picture
Traffic flows left → right: phone & tower (RAN) → the core's brains → the data gateway (UPF) → the internet.
5G Core Lab-in-a-Box · Field Guide
11

## Slide 12
LEFT SIDE · STEP 1
The RAN — the phone & the tower
RAN = Radio Access Network. In the diagram this is the purple box on the far left. It holds two things a real network keeps miles apart — here both are simulated by one program.
Everything a phone does to get online starts here and flows rightward into the core. The blue line leaving the tower (N1/N2) is the “let this phone on” conversation.
UE the handset + SIM
gNB the 5G radio tower
→ N1/N2 to the core
5G Core Lab-in-a-Box · Field Guide
12

## Slide 13
TOP CENTER · STEP 2
The Control Plane — the brains
The big blue box: the decision-makers. Think of them as the staff of a members' club — each does one job, and they talk over web technology (the “SBI” line).
AMF
The greeter / front desk — First contact from the tower; handles the phone joining and moving around.
AUSF · UDM · UDR
The ID desk & records — Check the SIM is genuine (authentication) and look up what it's allowed to do.
SMF
The session organizer — Sets up your internet session when you actually want to use data.
PCF · NSSF · NRF · SCP
The supporting staff — Rules & data limits, network “slicing,” the internal directory, and message routing.
5G Core Lab-in-a-Box · Field Guide
13

## Slide 14
BOTTOM CENTER · STEP 3
The UPF — the fast lane
The green box. Once the phone is approved, your data doesn't crawl through all that staff — it takes the express doorway straight through the UPF (User Plane Function).
Two lines touch it. Green (N3) carries your data in from the tower, tunneled. Blue-dashed (N4) is the SMF telling it how to handle the session.
SMF
session organizer
N4
UPF
the data gateway
N3 in
→ N6 out to the internet
5G Core Lab-in-a-Box · Field Guide
14

## Slide 15
PUTTING IT TOGETHER
Two journeys, end to end
The whole diagram is really just these two paths. Trace them and you understand 5G.
Your data · the green path
UE
radio
gNB
N3
UPF
N6
Internet
Setup & signaling · the blue path
gNB
N2
AMF
SBI
SMF
N4
UPF
Blue sets the phone up; green carries the data. Every other box supports one of these two.
5G Core Lab-in-a-Box · Field Guide
15

## Slide 16
BOTTOM OF THE DIAGRAM
What makes it a security lab
The coral box underneath hooks onto the two data-plane pipes — because N3 and N4 are exactly where a real attacker would strike.
attacks/
“inject”
Fires malformed or flood traffic at N3 and N4 — the realistic attack surface of a live 5G core.
capture/
“tap”
Records everything crossing N3 and N4, turning it into labeled data to train an anomaly detector.
Because the lab knows which attack is running, every capture is labeled automatically — clean training data.
5G Core Lab-in-a-Box · Field Guide
16

## Slide 17
PART 3
Reading the Security Loop
A guided tour of the attack-flow diagram.

## Slide 18
ORIENTATION
The diagram has two parts
Top strip — The security loop
One assembly line, left to right: make bad traffic → let it hit the core → record it → boil it down to numbers → let a model flag it. Follow the arrow labels: inject, tap, parse, score.
Bottom table — The attacks themselves
Five specific attacks. Each row reads: what it is → which pipe it hits → what it does → the number that gives it away. The colored bar shows the pipe: green N3, blue N4, purple N2.
5G Core Lab-in-a-Box · Field Guide
18

## Slide 19
THE FULL DIAGRAM
Attack & detection flow
5G Core Lab-in-a-Box · Field Guide
19

## Slide 20
THE TOP STRIP
The security loop — five steps
attacks/
Generate malformed
& flood traffic
inject
5G core
The live core
being attacked
tap
capture/
Record N3 + N4
to files (pcaps)
parse
extract_features
Boil each window
down to numbers
score
model → ALERT
Score each window,
flag anomalies
In one line: make bad traffic → let it hit the core → record it → turn it into numbers → let a model catch it.
5G Core Lab-in-a-Box · Field Guide
20

## Slide 21
THE CLEVER PART
“Labeled by construction”
To train a detector you need traffic tagged as “normal” or “attack.” Getting those labels is usually the hard part.
The usual way
A human hunts through millions of recorded packets and hand-tags which ones were attacks. Slow, tedious, and error-prone — and public datasets are scarce.
This lab
The lab launched the attacks, so it already knows exactly when each one ran. Every recorded window is stamped with the truth — automatically, for free.
vs
5G Core Lab-in-a-Box · Field Guide
21

## Slide 22
THE ATTACKS · 1 OF 2
On the data tunnel (N3)
Both target N3 — the pipe carrying user data. One breaks packets; the other overwhelms with volume.
N3 · GTP-U
malformed GTP-U
gtpu/malformed_gtpu.py
Broken packets
Sends deliberately malformed data — wrong type, garbage tunnel IDs, corrupted headers. Like mailing envelopes with nonsense addresses to jam the mailroom.
The tell: decode-failure rate spikes (gtpu_malformed_frac ↑)
N3 · GTP-U
GTP-U tunnel flood
gtpu/gtpu_flood.py
Too much, too fast
Not broken — just a firehose of data down a single tunnel, far more than normal.
The tell: packet rate & byte volume spike (pkt_rate · bytes_total ↑)
5G Core Lab-in-a-Box · Field Guide
22

## Slide 23
THE ATTACKS · 2 OF 2
On control & signaling (N4 · N2)
N4 · PFCP
PFCP session flood
A rapid burst of “start a new session” requests, trying to exhaust the core — like thousands slamming the front desk at once.
The tell: session-request count spikes (pfcp_est_req ↑)
N4 · PFCP
PFCP association abuse
Churns the standing handshake between the session-manager and the gateway, and fakes heartbeats.
The tell: abnormal association / heartbeat counts
N2 · NGAP
signaling storm
Floods the “greeter” (AMF) with endless join attempts, overwhelming the login desk.
The tell: registration rate spikes · (weakly caught today — N2 gap)
5G Core Lab-in-a-Box · Field Guide
23

## Slide 24
THE SMALL PRINT
Built-in safety rail
!
Every attack script refuses to run unless BOTH are true:
1. the target is your own lab — a loopback or private address, not a real network, and 2. you explicitly confirm it — by passing the --i-own-this-lab flag.
It's deliberate friction, so the tooling can't be casually pointed at anything but the lab you control.
5G Core Lab-in-a-Box · Field Guide
24

## Slide 25
THE WHOLE STORY
A working 5G network you can attack, capture, and learn from — safely, on one machine.
The network
Phone + tower + core, all in software.
The data path
Green carries data; blue sets it up.
The security loop
Inject → tap → parse → score; labeled for free.