## Slide 1
5G LAB-IN-A-BOX · N3/N4 ANOMALY DETECTION
Detecting 5G Attacks
on the GPU
How the detector learns “normal” user-plane traffic and flags GTP-U / PFCP attacks — trained on the NVIDIA DGX Spark (GB10).
1.000
ROC-AUC (GPU model)
100%
attack recall
5 classes
N3 + N4
Notes: This deck explains, from the ground up, how the GTP/PFCP anomaly detector works: the data, how the model trains on the GPU, the test results as proof, and how to read those numbers honestly. Audience: technical peers; we teach the ML concepts as we go.

## Slide 2
THE THREAT
What we’re detecting: attacks on the 5G user plane
The UPF terminates the user plane. Two interfaces carry the traffic we watch — and the traffic an attacker abuses:
N3
GTP-U · UDP 2152
Carries user data in GPRS tunnels between the gNB and the UPF.
N4
PFCP · UDP 8805
Control between the SMF and UPF — sets up and tears down sessions.
Four attack classes exercised against the UPF:
!
gtpu_flood
N3 volumetric tunnel flood — the anomaly is rate & volume.
!
gtpu_malformed
N3 malformed GTP-U — the anomaly is packet structure.
!
pfcp_session_flood
N4 session-establishment flood — control-plane pressure.
!
pfcp_assoc_abuse
N4 association churn — repeated setup / teardown.
These map to real MNO user-plane risk: tunnel abuse, resource exhaustion, and parser attacks on the UPF.
Notes: The UPF is the target. N3 (GTP-U) is user data; N4 (PFCP) is SMF<->UPF control. Two of our attacks are on N3 (a volume flood and a malformed-packet attack — different anomaly signatures), two on N4 (session flood and association churn).

## Slide 3
THE APPROACH
Learn “normal,” then flag the unfamiliar
✗
Signature / supervised
Needs labeled examples of every attack. Blind to anything new. Attack space is open-ended — you can’t enumerate it.
✓
Anomaly / semi-supervised
Train only on benign traffic — which is abundant. Anything that departs from normal is suspicious, including attacks never seen before.
The key move
We never show the model an attack during training. It learns only what benign N3/N4 looks like — so an attack stands out precisely because the model has no template for it.
Notes: Why semi-supervised: labeled attacks are scarce and the attack space is unbounded, but benign traffic is plentiful. So we model normal and treat distance-from-normal as the alarm signal. This is the standard framing for network anomaly detection.

## Slide 4
THE DATA — WHERE IT COMES FROM
Captured at the UPF, the way a real UPF sees it
UE
gNB → benign N3
!
attacker container
UPF
N3 GTP-U : 2152
N4 PFCP : 8805
●
Capture point
Inside the UPF network namespace (nsenter + tcpdump)
Benign baseline = real UE traffic (ping over the data tunnel) — genuine N3 GTP-U.
Attacks = the four classes, each fired from a throwaway container at the UPF.
We tap N3 + N4 from inside the UPF’s own netns — the authoritative user-plane view, exactly what a production UPF observes.
Notes: Capturing from the UPF's network namespace (via nsenter, using the host's tcpdump) is the honest vantage point — it's the traffic the UPF actually receives on N3/N4. Benign is real UE traffic; each attack is a container on the same docker network aimed at the UPF.

## Slide 5
THE DATA — PACKETS TO FEATURES
One row of numbers per 1-second window
1
pcap
raw N3/N4 packets
2
window
slice into 1.0s bins
3
features
numeric row per bin
4
labeled table
585 rows
What each window captures
Packet rate & byte rate (volume signal for floods)
Mean / spread of packet size (structure signal)
N3 vs N4 port mix (which interface is active)
Distinct TEIDs / peer addresses (tunnel churn)
PFCP message-type counts (session vs association)
Labeling is automatic
Each capture file is named for the traffic that was running:
gtpu_flood_20260730-….pcap → label = gtpu_flood
So a folder of captures becomes a labeled dataset with no manual tagging.
Notes: We turn packets into a compact numeric fingerprint per one-second window: rates, sizes, port mix, tunnel/peer churn, PFCP message types. The window's label comes from the pcap filename, which encodes which traffic was running — so extraction yields a labeled table directly. Result: 585 windows.

## Slide 6
THE DATASET
585 windows — and a benign-only training set
585
total windows
5
traffic classes
143
benign — training
442
held-out — test
Chart: 
| benign | gtpu_flood | gtpu_malformed | pfcp_assoc_abuse | pfcp_session_flood
windows | 239 | 86 | 87 | 86 | 87
Why train on benign only?
The model builds a picture of normal from the 143 benign windows.
It is then judged on 442 unseen windows — held-out benign plus every attack.
Attacks appear only at test time, so high scores can’t be memorization.
Notes: 585 windows, five labels (benign is the majority). We train the detector on 143 benign windows only, and evaluate on a held-out mix of 442 (benign + all four attack classes). Because attacks are absent from training, detecting them is a genuine generalization test, not recall of memorized examples.

## Slide 7
ML PRIMER · THE MODEL
An autoencoder learns to rebuild “normal”
AE
The intuition
Like learning to sketch faces you’ve seen a thousand times: something familiar comes back cleanly; something it has never seen comes back distorted.
input
features
encoder
compress
code
bottleneck
decoder
expand
output
reconstruction
Trained so that output ≈ input on benign windows.
Small PyTorch MLP: 4 layers, an 8-unit bottleneck, MSE loss.
Notes: An autoencoder squeezes each input through a narrow bottleneck and tries to reconstruct it. Trained only on benign, it becomes good at rebuilding normal traffic and bad at rebuilding anything else. It's a small MLP here; the same idea scales to sequence/graph variants later.

## Slide 8
ML PRIMER · THE SCORE
Reconstruction error is the anomaly score
Feed a window in, read the rebuilt version out, measure how far off it is (mean squared error).
Benign windows rebuild well → low error. Attack windows rebuild poorly → high error.
Set the alarm threshold at the 99th percentile of benign error. Above the line → flagged.
reconstruction error →
benign
attack
99th-pct
threshold
Notes: The score is just how badly the model rebuilt the window. Benign errors cluster low; attack errors sit high. We draw the line at the 99th percentile of benign error — so ~1% of benign is expected to trip it — and flag anything above. This is the operating threshold you can later tune.

## Slide 9
TRAINING ON THE GPU
The training loop, running on the GB10
1
Standardize
scale benign features to comparable ranges
2
Forward
reconstruct each benign window
3
Loss
MSE between input and reconstruction
4
Backprop
Adam updates weights
5
Repeat
80 epochs — benign rows only
GPU
Auto-detects CUDA
model + tensors move to the GPU
torch 2.11.0 + cu128
device: NVIDIA GB10
Why the GPU matters
At 585 windows GPU vs CPU is negligible. The point: the same pipeline now trains on the GB10, so scaling to large captures and deeper sequence / graph models offloads to the GPU.
Notes: Standard training loop: standardize, forward pass, MSE loss, Adam backprop, 80 epochs, benign only. The code auto-detects CUDA and moves the network and tensors onto the GB10. Honest framing: this dataset is tiny so the GPU isn't stressed — the value is that the pipeline is now GPU-native for when data and models grow.

## Slide 10
A SECOND OPINION
Cross-check: an IsolationForest baseline
IF
The intuition
Outliers are easy to isolate: a few random splits fence off an odd point far faster than a point buried in the crowd. Fewer splits to isolate = more anomalous.
How it works
Tree-based, unsupervised, CPU. Fit on benign; score = how quickly a window is isolated by random partitioning.
Why run two models
A fast, independent method to sanity-check the neural detector. When both agree, confidence in the signal goes up.
Two lenses on the same question
The autoencoder learns a smooth model of normal; the forest partitions the space. Different mechanisms, same verdict on our data — a stronger result than either alone.
Notes: IsolationForest is our second, independent detector: tree-based, CPU, unsupervised. It isolates outliers with random splits — fewer splits means more anomalous. Running two very different methods and getting the same answer is more convincing than one model alone.

## Slide 11
ML PRIMER · HOW WE SCORE IT
The metrics, in plain terms
1
ROC-AUC
Separability, independent of any threshold. 1.0 = benign and attack scores never overlap; 0.5 = coin flip.
2
Recall (attacks)
Of all attack windows, the fraction we flagged. Misses are the cost of low recall.
3
Precision
Of everything we flagged, the fraction that were truly attacks. Low precision = noisy alarms.
4
False-alarm rate
Benign windows wrongly flagged. This is the operational tax of the detector.
5
F1
Single number balancing precision and recall.
6
Threshold
The line on the score. Move it to trade recall against false alarms.
Notes: The metrics: ROC-AUC measures separability regardless of threshold; recall is the fraction of attacks caught; precision is how clean the alarms are; false-alarm rate is benign wrongly flagged; F1 balances precision and recall. The threshold is the knob that trades recall against false alarms.

## Slide 12
THE PROOF
Results on 442 held-out test windows
Model | Device | ROC-AUC | Precision | Recall | F1 | Benign false-alarm
IsolationForest | CPU | 0.989 | 0.975 | 1.000 | 0.987 | 9.4%
Autoencoder | GB10 GPU | 1.000 | 0.986 | 1.000 | 0.993 | 5.2%
Per-class recall = 1.000 across all four attack classes:
✓
gtpu_flood
✓
gtpu_malformed
✓
pfcp_assoc_abuse
✓
pfcp_session_flood
1.000
The GPU-trained autoencoder perfectly separates benign from attack on the test set, and both detectors catch every attack window — while flagging only ~5% of benign traffic.
Notes: The proof: on 442 held-out windows, the GPU autoencoder reaches ROC-AUC 1.000, the IsoForest 0.989; both catch 100% of attacks across all four classes. Benign false-alarm is 5.2% (autoencoder) / 9.4% (isoforest). Next slide: what these numbers do and don't mean.

## Slide 13
HOW TO READ IT
Interpreting the numbers — honestly
✓
ROC-AUC 1.000
On this test set, benign and attack scores don’t overlap at all — perfect separation. A threshold exists that splits them cleanly.
✓
Recall 100%
Every attack window was flagged. No misses on any of the four classes.
✓
False-alarm 5.2%
About 1 benign window in 20 trips the alarm. Tunable: raise the threshold to cut it (at some recall risk).
!
Read the ceiling, not the hype
A perfect score on a small, clean lab set is expected — these attacks are loud and distinct. It proves the pipeline detects known-loud attacks end-to-end. It is a floor to build on, not a claim of production accuracy.
Perfect numbers are a reason to test harder, not to stop.
Notes: Interpretation, honestly: 1.000 means the two score distributions don't overlap on this set; 100% recall means no missed attack windows; 5.2% false-alarm means ~1 in 20 benign flagged, tunable via threshold. The caution: a perfect score on a small clean lab dataset is expected because the attacks are loud — it validates the pipeline, it doesn't claim production accuracy.

## Slide 14
SCOPE & LIMITS
What this does — and doesn’t — prove
1
Lab-clean data
585 windows, distinct attacks. Real traffic is noisier and more varied.
2
Benign must be representative
Semi-supervised: if the benign baseline is narrow, novel-but-legit traffic looks anomalous.
3
User plane only
N3 / N4 scope. N2 signaling storms are out of frame for this detector.
4
Perfect → stress it
Loud attacks are easy. Subtle, low-and-slow abuse and larger captures are the real test.
These are the hardening backlog, not flaws in the method — each points at a concrete next experiment.
Notes: Honest limits: the data is lab-clean and the attacks are loud; the semi-supervised approach assumes a representative benign baseline; scope is N3/N4 only (not N2 signaling); and perfect scores mean we should stress the detector with subtler attacks and larger, noisier captures. These define the next experiments.

## Slide 15
WHAT THIS PROVES
An end-to-end detector, trained on the GPU
Capture → features → GPU-trained model → validated — the whole pipeline runs on ARM64 + the GB10.
Both detectors catch every attack class; the GPU autoencoder separates benign from attack perfectly on the test set.
The training path is now GPU-native, ready to scale.
Next
1
Scale the capture
larger, noisier, longer
2
Phase-5 models
sequence / graph on the GB10
3
Stress it
subtle, low-and-slow attacks
4
Tune threshold
to a false-alarm budget
5G Lab-in-a-Box · GTP/PFCP anomaly detection on the NVIDIA DGX Spark
Notes: Bottom line: capture, feature extraction, and GPU model training run end-to-end on ARM64 + the GB10, and the detector catches every attack class on the test set. The pipeline is now GPU-native. Next: scale the data, add the heavier Phase-5 sequence/graph models that actually stress the GPU, stress-test with subtler attacks, and tune the threshold to the operational false-alarm budget.