## Slide 1
TEST RUN REPORT
Did the Lab Actually Catch the Attacks?
A plain-language walkthrough of the first detection run on real 5G traffic — what we did, what happened, and what to try next.

## Slide 2
THE QUESTION
What we were testing
Can a computer model, trained only on normal 5G traffic, spot attacks it's shown later?
Record
capture the traffic
on the core's pipes
Summarize
boil each second
down to numbers
Learn normal
model studies what
normal looks like
Flag
anything abnormal
raises an alert
If it flags the attacks but leaves normal traffic alone, the approach works.
First Detection Run — Test Report
2

## Slide 3
THE PROCEDURE
How the test ran
1
Generated traffic
Ran steady normal traffic plus four different attacks against the lab's own 5G core.
2
Recorded it
Captured everything on the core's internal N3 / N4 pipes — the data tunnel and the control link.
3
Summarized it
Sliced the recordings into one-second windows and reduced each to a handful of numbers.
4
Trained & tested
Let the model learn from “normal,” then checked whether it flags the attack windows it hadn't trained on.
Result: 270 one-second windows across 5 traffic types — 1 normal + 4 attacks — all automatically labeled by the lab.
First Detection Run — Test Report
3

## Slide 4
ATTEMPT 1
The first try flopped — and taught us something
The model did worse than a coin flip. The reason was simple: we'd given it only 10 examples of “normal.” That's not enough to learn what normal looks like, so it couldn't tell normal from attack.
0.355
separation score
below 0.5 = worse than random guessing
0%
of attacks caught
it flagged essentially nothing
43%
false alarms
and it mis-flagged normal traffic too
Lesson: a detector is only as good as its picture of “normal.”
First Detection Run — Test Report
4

## Slide 5
ATTEMPT 2 · THE RESULTS
With enough “normal,” it worked
We recorded ~2 minutes of steady normal traffic (68 examples instead of 10), retrained, and the results flipped:
0.958
separation score
how well it tells attack from normal (1.0 = perfect)
100%
of attacks caught
every window of all four attack types flagged
6.5%
false alarms
on normal traffic — and this is a tunable dial
Every attack type was caught:
100%
Malformed GTP-U
100%
GTP-U flood
100%
PFCP session flood
100%
PFCP assoc. abuse
First Detection Run — Test Report
5

## Slide 6
IMPLICATIONS
What the results mean
The whole pipeline works
Record → summarize → detect runs end to end on real captured traffic — not a mock-up or a simulation.
It reliably tells attack from normal
A 0.958 separation score with every attack type caught means the signal is strong and consistent, not luck.
The approach is proven
A 5G core can be watched, and attacks flagged, by a model trained on the core's own traffic. That's the core idea — validated.
First Detection Run — Test Report
6

## Slide 7
STAYING HONEST
What it does NOT prove (yet)
A strong proof of concept — but not production accuracy. Four things to keep in mind:
Lab-made, very clean
Both normal and attack traffic were generated in the lab, and the types were very distinct — so they separate more easily than messy real-world traffic would.
One attack type untested
The “signaling storm” attack wasn't in this run — the recorder doesn't watch that particular pipe (N2) yet.
It flags, it doesn't name
The model says “this looks abnormal,” but doesn't yet say which attack it is.
Not yet real-world data
To trust it on a live network, it needs training on real, varied normal traffic — a data-collection job for later.
First Detection Run — Test Report
7

## Slide 8
FUTURE EXPERIMENTS
Tweaks to try next
Each is a knob we can turn to push the results further:
Experiment
What it would improve
Adjust the sensitivity dial
Trade off fewer false alarms vs. catching subtler attacks (the “contamination” setting).
Richer, more varied “normal”
Results that hold up outside the lab — the single biggest lever on real-world quality.
Teach it to name the attack
Alerts that say which attack it is, not just “something's off” — far more actionable.
Watch the N2 pipe too
Adds coverage for the signaling-storm attack that's currently invisible.
Bigger models (DGX Spark)
Catch slow, subtle attacks that the simple model misses.
First Detection Run — Test Report
8

## Slide 9
BOTTOM LINE
The lab caught every attack it was shown — a working proof of concept.
Record the traffic, learn what normal looks like, and the attacks stand out. Next: make “normal” richer and the alerts smarter.
0.958
separation score
100%
attacks caught
6.5%
false alarms